## Slide 1
林俊曄
2022/10/13 (四)
HW2
Enigma
EE4292 IC Design Laboratory

## Slide 2: Introduction
Enigma
  The electro-mechanical rotor cipher machine
  Used by German military in World War II
  Two operation mode:
    Encrypt:
      Input: 6-bits plaintext, Output: 6-bits ciphertext
      E.g., Do you → ut.hDd
    Decrypt:
      Input: 6-bits ciphertext, Output: 6-bits plaintext
      E.g., ut.hDd → Do you
EE4292 IC Design Laboratory
image ref: https://en.wikipedia.org/wiki/Enigma_machine

## Slide 3: Enigma FSM
IDLE state:
  Do not thing
LOAD state:
  Initialize rotors
READY state:
  Perform encryption or decryption
EE4292 IC Design Laboratory

## Slide 4: Enigma Mechanism Overview
Flow:
Forward rotor mapping + Inverse rotor mapping
Forward rotor mapping (solid arrows)
  Input: index; Output: value
Inverse rotor mapping (dotted arrows)
  Input: value; Output: index
EE4292 IC Design Laboratory

## Slide 5: Toy Example (6 symbols)
Structure: Rot + Ref (Fixed)
Rot[6] = {01, 02, 03, 00, 05, 04}
Ref[6] = {05, 04, 03, 02, 01, 00}
symbol | hex num
a | 00
b | 01
c | 02
d | 03
e | 04
f | 05
toy ascii table
b
c
d
a
f
e
idx
00
01
02
03
04
05
Rot
f
e
d
c
b
a
idx
00
01
02
03
04
05
Ref

## Slide 6: Encrypt “e”
b
c
d
a
f
e
toy ascii
table
00
01
02
03
04
05
Rot
f
e
d
c
b
a
Ref
a
b
c
d
e
f
EE4292 IC Design Laboratory

## Slide 7: Decrypt “d”
b
c
d
a
f
e
toy ascii
table
00
01
02
03
04
05
Rot
f
e
d
c
b
a
Ref
a
b
c
d
e
f
EE4292 IC Design Laboratory

## Slide 8: Enigma Structure
Plug Board x 1
  Not fixed
Rotors x 2
  Not fixed
Reflector x 1
  Fixed
EE4292 IC Design Laboratory
Structure of our Enigma
If all tables are fixed, than the encryption would be easy to crack !

## Slide 9: Plug Board (PB)
The PB doesn’t move after initialization.
One line connects two letters together.
There are 16 lines on PB.
EE4292 IC Design Laboratory
image ref: https://piotte13.github.io/enigma-cipher/
a
b
c
d
e
···
_
···
&
+
00
01
02
03
04
···
61
···
63
62
idx
value
d
b
c
a
e
···
_
···
&
+
00
01
02
03
04
···
61
···
63
62
idx
value
d
c
b
a
&
···
_
···
e
+
00
01
02
03
04
···
61
···
63
62
idx
value
···
PB behavior in LOAD state

## Slide 10: RotorA (RotA)
EE4292 IC Design Laboratory
RotA receives the initial permutation (i.e., ) in LOAD state.
Depending on different RotA modes, RotA shifts right 0-3 symbols after encrypting one symbol.
In encryption operation, the least significant two bits of the rotA output are used to decide rotA mode.
e.g.,
rotA output = ‘_’ = 6’b111101
→ rotA mode1 (i.e. shift right 1)
j
X
E
g
?
···
e
···
Y
W
00
01
02
03
04
···
61
···
63
62
idx
value
00
01
02
03
04
···
61
···
63
62
idx
value
shift right 1
Y
j
X
E
g
···
Q
···
W
e
00
01
02
03
04
···
61
···
63
62
idx
value
shift right 3
Q
e
W
Y
j
···
G
···
c
I
mode 1
(‘_’ = 6’b111101)
mode 3
(‘l’ = 6’b001011)
mode 1
(‘J’ = 6’b101001)
shift right 1
RotA behavior in READY state

## Slide 11: RotorB (RotB)
RotB has two-stage adaptive permutation after each symbol encryption/ decryption.
  First stage: S-Box8 permutation
  Second stage: S-Box64 permutation
RotB receives the initial permutation (i.e., ) in LOAD state.
EE4292 IC Design Laboratory

## Slide 12: RotB First Stage: S-Box8
EE4292 IC Design Laboratory
The S-Box8 applies for each eight contiguous symbols and has eight possible modes.
In encryption, the modes are decided by the least significant three bits of the rotB output.
(e.g., ‘a’ = 6’b000000 → mode 0)

## Slide 13: RotB First Stage: S-Box8
EE4292 IC Design Laboratory

## Slide 14: RotB Second Stage: S-Box64
EE4292 IC Design Laboratory
The second-stage S-Box64 follows a fixed permutation as shown in the following figure.

## Slide 15: RotB Second Stage: S-Box64
EE4292 IC Design Laboratory

## Slide 16: Reflector (Ref)
EE4292 IC Design Laboratory
The reflector is a fixed table that has the reverse order of the ASCII table.

## Slide 17: Step in this homework
EE4292 IC Design Laboratory
Part1 (rotA + ref) (2%)
Part2 (rotA + rotB + ref) (4%)
Part3 (PB + rotA + rotB + ref) (4%)
Note: Your testbench must follow the reference waveform. Otherwise, your RTL codes might not pass the simulation when TA uses his testbench to evaluate.

## Slide 18: Part1 (rotA + ref) (2%)
EE4292 IC Design Laboratory
Given the behavior model, implement the testbench test_enigma_part1.v for encrypting patten1 (1%).
Change the behavior model to your synthesizable RTL code enigma_part1.v (1%)
Note: Execute part1/sim/run_rtl.sh to check all the cases in Part1.

## Slide 19: Part2 (rotA + rotB + ref) (4%)
EE4292 IC Design Laboratory
Implement the synthesizable Enigma RTL code enigma_part2.v (2%)
Write the testbench test_enigma_part2.v for encrypting/ decrypting pattern1-2 (2%)
Note: Execute part2/sim/run_rtl.sh to check all the cases in Part2.

## Slide 20: Part3 (PB + rotA + rotB + ref) (4%)
EE4292 IC Design Laboratory
Implement the synthesizable Enigma RTL code enigma_part3.v (2%)
Write the testbench test_enigma_part3.v for encrypting/ decrypting pattern1-2 (1%)
Write the testbench test_enigma_part3_display.v to decrypt and save the results of pattern2-3 in ASCII format (1%)
Note: Execute part3/sim/run_rtl.sh and part3/sim/run_display.sh to check all the cases in part3.

## Slide 21: Part3 Cont’d
You need to decrypt and save pattern2-3 in ASCII format.
You can refer to display_enigma_code.v and show_enigma_code.v for displaying ASCII decrypted texts.
e.g.,
$vcs –R +v2k –full64 show_enigma_code.v +define+PAT1
$vcs –R +v2k –full64 show_enigma_code.v +define+PAT2

## Slide 22: Notices
EE4292 IC Design Laboratory
Your testbench must follow the reference waveform. Otherwise, your RTL codes might not pass the simulation when TA uses his testbench to evaluate.
TA will use unreleased patterns to evaluate your homework. Therefore, Do not design your hardware by the given datasets.
e.g., Different 16 lines for PB connection

## Slide 23: Submission
Deadline
  10/27 11:59 p.m.
Submit to eeclass
  Make sure the file delivery and organization meet the requirement
  Wrong file delivery or organization will get 1% punishment
If you have any question
  Feel free to ask on eeclass discussion
  (maybe other students also have the same question!)
  Do not show your code or email your code to TA.
  Coding by yourself!
EE4292 IC Design Laboratory

## Slide 24: Appendix
https://www.youtube.com/watch?v=ybkkiGtJmkM&t=202s&ab_channel=JaredOwen
EE4292 IC Design Laboratory